## Slide 1
MQTT
Message Queuing Telemetry Transport
http://mqtt.org/

## Slide 2: MQTT - Open Connectivity for Mobile, M2M and IoT
1999 Invented by Dr. Andy Stanford-Clark (IBM),
Arlen Nipper (now Cirrus Link Solutions)
2011 - Eclipse PAHO MQTT open source project
2004 MQTT.org open community
2013 – MQTT Technical Committee
formed
Cimetrics, Cisco, Eclipse, dc-Square, Eurotech, IBM, INETCO Landis & Gyr, LSI, Kaazing, M2Mi, Red Hat, Solace, Telit Comms, Software AG, TIBCO, WSO2
Evolution of an open technology
▶ MQTT and MQTT-SN are lightweight publish/subscribe messaging transports for TCP/IP and connectionless protocols (such as UDP) respectively. The Eclipse Paho project provides open source, mainly client side, implementations of MQTT and MQTT-SN in a variety of programming languages.
▶ A lightweight publish/subscribe protocol with predictable bi-directional
message delivery

## Slide 3: MQTT
▶ MQTT is described on the mqtt.org site as a machine-
to-machine (M2M) / IoT connectivity protocol.
▶ MQTT is an Event based IoT middleware (one to many)
▶ publish/subscribe messaging transport protocol
▶ Over TCP/IP (or MQTT-S over UDP for LAN)
▶ Its protocol is lightweight
▶ it can be supported by some of the smallest measuring
and monitoring devices (ex. Arduino)
▶ it can transmit data over far reaching networks
▶ It can transmit data over sometimes intermittent networks.
Event based IoT Middleware
Event pattern of communication (one to many)
Over IP (TCP)

## Slide 4: Publish / Subscribe Messaging (One to Many)
▶ A producer publishes a message (publication) on a topic (subject)
▶ A consumer subscribes (makes a subscription) for messages on a topic (subject)
▶ A message server (called BROKER) matches publications to subscriptions
▶ If none of them match the message is discarded after modifying the topic
▶ If one or more matches the message is delivered to each matching consumer after
modifying the topic
▶ Publish / Subscribe has three important characteristics:
It decouples message senders and receivers, allowing for more flexible applications
It can take a single message and distribute it to many consumers
This collection of consumers can change over time, and vary based on the nature of the message.
Server

## Slide 5: MQTT Topic and Wildcards

## Slide 6: MQTT Topic : Details
A topic forms the namespace
▶ Is hierarchical with each “sub topic” separated by a /
▶ An example topic space
▶ A house publishes information about itself on:
▶ <country>/<region>/<town>/<postcode>/<house>/energyConsumption
▶ <country>/<region>/<town>/<postcode>/<house>/solarEnergy
▶ <country>/<region>/<town>/<postcode>/<house>/alarmState
▶ <country>/<region>/<town>/<postcode>/<house>/alarmState
▶ And subscribes for control commands:
▶ <country>/<region>/<town>/<postcode>/<house>/thermostat/setTemp
A subscriber can subscribe to an absolute topic or can use wildcards:
▶ Single-level wildcards “+” can appear anywhere in the topic string
▶ Multi-level wildcards “#” must appear at the end of the string
▶ Wildcards must be next to a separator
▶ Cannot be used wildcards when publishing
▶ For example
▶ UK/Hants/Hursley/SO212JN/1/energyConsumption
▶ Energy consumption for 1 house in Hursley
▶ UK/Hants/Hursley/+/+/energyConsumption
▶ Energy consumption for all houses in Hursley
▶ UK/Hants/Hursley/SO212JN/#
▶ Details of energy consumption, solar and alarm for all houses in SO212JN

## Slide 7: MQTT publish subscribe architecture
▶ The MQTT messages are delivered asynchronously (“push”) through publish subscribe architecture.
▶ The MQTT protocol works by exchanging a series of MQTT control packets in a defined way.
▶ Each control packet has a specific purpose and every bit in the packet is carefully crafted to reduce the data transmitted over the network.
▶ A MQTT topology has a MQTT server and a MQTT client.
▶ MQTT client and server communicate through different control packets. Table below briefly describes each of these control packets.

## Slide 8: Sample of protocol use

## Slide 9: Ideal for constrained networks (low bandwidth, high latency, data limits, and fragile connections)
▶ MQTT control packet headers are kept as small as possible.
▶ Each MQTT control packet consist of three parts, a fixed header, variable header and payload.
▶ Each MQTT control packet has a 2 byte Fixed header. Not all the control
packet have the variable headers and payload.
▶ A variable header contains the packet identifier if used by the control packet.
▶ A payload up to 256 MB could be attached in the packets.
▶ Having a small header overhead makes this protocol appropriate for IoT by
lowering the amount of data transmitted over constrained networks.

## Slide 10: Quality of Service (QoS) for MQTT
▶ Quality of service (QoS) levels determine how each MQTT message is delivered and must be specified for every message sent through MQTT.
▶ Three QoS for message delivery could be achieved using MQTT:
▶ QoS 0 (At most once) - where messages are delivered according to the best efforts of the operating environment. Message loss can occur.
▶ QoS 1 (At least once) - where messages are assured to arrive but duplicates can occur.
▶ QoS 2 (Exactly once) - where message are assured to arrive exactly once.
▶ There is a simple rule when considering performance impact of QoS :
“The higher the QoS, the lower the performance".

## Slide 11: Quality of Service (QoS) for MQTT

## Slide 12: MQTT Clients and APIs
▶ You can develop an MQTT client application by programming directly to the MQTT protocol specification …… however it is more convenient to use a prebuilt client
▶ Open Source clients available in Eclipse Paho project
▶ C, C++, Java, JavaScript, Lua, Python and Go
▶ Clients for other languages are available, see mqtt.org/software
▶ E.g. Delphi, Erlang, .Net, Objective-C, PERL, PHP, Ruby
▶ Not all of the client libraries listed on mqtt.org are current. Some are at an early or experimental stage of development, whilst others are stable and mature.
▶ Even in shell script like we are seeing in the practical course …